## Slide 1: Introduction to Computer Architecture Project 3
MIPS Simulator (Part 2)

## Slide 2: Project 3 Overview
In Project 3, you’ll need to implement the remaining parts of the MIPS instruction simulator

## Slide 3: Instructions to Support (1)
All instructions from Project 2
Multiply/Divide: div, divu, mfhi, mflo, mthi, mtlo, mult, multu
Memory access: lw, lh, lhu, lb, lbu, sw, sh, sb
Branch and Jump: jalr, jr, j, jal, beq, bne
System call instruction: syscall

## Slide 4: Instructions to Support (2)
Some hints on mult / multu
  In C programming language, in order to obtain 64-bit results from multiply operation, cast the value to a 64-bit integer, and then perform multiply.
    mult: use signed 64 bit integer
    multu: use unsigned 64 bit integer

## Slide 5: Data Structures to Implement
From Project 2,
  Registers
    Now, you need to model the HI and LO registers as well
  Instruction memory
Data memory
  Unlike real CPU, data memory is separated from instruction memory
  Data memory address range: 0x10000000 – 0x10010000 (64KB)
  All contents are initialized to 0xFF at beginning

## Slide 6: Requirement #1: Data Loading
Add the following commands to your program
  loadinst <filename>
    Same as Project 2
  loaddata <filename>
    Read the binary file named <filename> and store the binary data to the data memory
    Always start from data memory address 0x10000000
    DO NOT try to convert the endianness
      i.e., The first byte in the file should be stored at data memory address 0x10000000, and the second byte should be stored at 0x10000001, …

## Slide 7: Requirement #2: Instruction Execution
Add the following command to your program
  run <N>
    Same as Project 2

## Slide 8: Requirement #3: Register Print
Add the following command to your program
  registers
    Print the current value of registers ($0-$31, HI, LO, and PC)
    Basically the same as project 2, but add HI and LO
mips-sim> registers
$0: 0x00000000
$1: 0x00000000
$2: 0x0000000a
$3: 0x00000014
$4: 0x10000004
$5: 0x1000002c
$6: 0x00000000
$7: 0x00000000
$8: 0x00000000
$9: 0x00000000
$10: 0x00000000
$11: 0x00000000
$12: 0x00000000
$13: 0x00000000
$14: 0x00000000
$15: 0x00000000
$16: 0x00000000
$17: 0x00000000
$18: 0x00000000
$19: 0x00000000
$20: 0x00000000
$21: 0x00000000
$22: 0x00000000
$23: 0x00000000
$24: 0x00000000
$25: 0x00000000
$26: 0x00000000
$27: 0x00000000
$28: 0x00000000
$29: 0x0fffffd0
$30: 0x0fffffd0
$31: 0x00000370
HI: 0x00000000
LO: 0x00404fa0
PC: 0x0000037c
mips-sim>

## Slide 9: Requirement #4: Memory – Error Handling
Case 1: If instruction fetch (PC) or load/store instruction tries to access an address out of the valid range, print the following error message and stop execution
  Memory address out of range: 0xXXXXXXXX
  “0xXXXXXXXX” is the address the CPU was trying to access
  Instruction memory valid range: 0x00000000 – 0x00010000
  Data memory valid range: 0x10000000 – 0x10010000
Case 2: If the address of the lw or sw instruction’s memory address is not a multiple of 4, print the following error message and stop execution
  Memory address alignment error: 0xXXXXXXXX
  “0xXXXXXXXX” is the address the CPU was trying to access
  For lh and sh, do the same check for address not multiple of 2
If the address violates both case 1 and case 2, print the error message for case 1

## Slide 10: Requirement #5: Syscalls
Similar to the MARS simulator, your simulator needs to provide some “pseudo” system calls
If your simulated CPU is executing the “syscall” instruction, check the current value $v0($2) and do the following
  If $v0=1, print the contents of $a0($4) in the signed integer format (“%d”).
    Do not add a newline!
  If $v0=4, print the string in the data memory pointed by $a0($4).
    Print until you encounter a NULL character
    Also, do not add a newline unless the string itself has a newline
  If $v0=10, print the following message and stop the simulation
    EXIT syscall
  Do not need to implement other system calls
    Print Invalid syscall and exit
mips-sim> run 1000
EXIT syscall
Executed 592 instructions
mips-sim>

## Slide 11: Test Sample
6 testcases are provided
  Test1: test on mult/div
    Instruction binary: ~swe3005/2020s/proj3/test1_t.dat
    No data to load
    Explanation and expected output: ~swe3005/2020s/proj3/test1_dis.txt
  Test2: test on load/store
    Instruction binary: ~swe3005/2020s/proj3/test2_t.dat
    Data: ~swe3005/2020s/proj3/test2_d.dat
    Explanation and expected output: ~swe3005/2020s/proj3/test2_dis.txt
  Test3: test on branch
    Instruction binary: ~swe3005/2020s/proj3/test3_t.dat
    No data to load
    Explanation and expected output: ~swe3005/2020s/proj3/test3_dis.txt
  Test4: test on system calls
    Instruction binary: ~swe3005/2020s/proj3/test4_t.dat
    Data: ~swe3005/2020s/proj3/test4_d.dat
    Explanation and expected output: ~swe3005/2020s/proj3/test4_dis.txt
  Test5: test on jump
    Instruction binary: ~swe3005/2020s/proj3/test5_t.dat
    No data to load
    Explanation and expected output: ~swe3005/2020s/proj3/test5_dis.txt
  Test6: Bubble sort
    Instruction binary: ~swe3005/2020s/proj3/test6_t.dat
    Data: ~swe3005/2020s/proj3/test6_d.dat
    Expected output: ~swe3005/2020s/proj3/test6_dis.txt

## Slide 12: Submission
Clear the build directory
  Do not leave any executable or object file in the submission
Use submit program
  If you want to submit “src” directory…
    ~swe3005/bin/submit proj3 src
Verify the submission
  ~swe3005/bin/check-submission proj3
Submitted Files for proj3:
File Name File Size Time
--------------------------------------------------------------------------------
proj3-2019123456-Sep.05.17.22.388048074 268490 Thu Sep 5 17:22:49 2019

## Slide 13: Project 3 Due Date
2020 May 27th, 23:59:59
Late penalty (max 3 days): 20% per day